## Slide 1: Pre-Task Planning The JSA Process
Note – Some slides are narrated. Have volume set at appropriate level

## Slide 2: Objectives
Explain the proper method to perform a JSA
Understand the expectations of the JSA process
Familiarize you with the JSA
Using the JSA Supplement for high risk or specialty work
Complete a JSA for a simulated task.

## Slide 3: What is a Job Safety Analysis?
  An incident prevention procedure that requires a supervisor to provide sufficient instruction to adequately integrate safety into the job.
  Method of identifying hazards
  Means of breaking the job process down
  System for employees to stop and assess their job for hazards
  Allows employees to identify all hazards and list how they are going to reduce or eliminate them
All task steps must be listed
All recognized hazards must be identified
Protective measures applied

## Slide 4: Why do we do JSA’s?
Identify existing hazards
Identify potential hazards
Reduce and/or eliminate hazards
Communicate safe work methods
Identify specific tools, equipment, or PPE
Identify any special certifications or permits
An integral part of the Target Zero philosophy

## Slide 5: What Tasks Require a JSA?
A Job Safety Analysis (JSA) is required for all tasks, no matter how minor.
Performing the Job Safety Analysis everyday for every job will keep the job in order for the best results without incident.
The Job Safety Analysis should be task and location specific.

## Slide 6: Steps in Preparing a JSA
Step
2
Break the job down into successive steps or activities and visualize how these actions are performed
Step
3
Identify the hazards and potential incidents for each step
Step
4
List how you are going to eliminate or reduce the hazards and prevent potential incidents
Step
1
Select the job to be analyzed
Involve Everyone

## Slide 7: Breaking Down the Task
List each job step in order of occurrence
Examine each step for hazards
Conduct a “what if” scenario for each step

## Slide 8: Hazards to Focus On
Working at height
Line of fire
Pinch points
Tool operations
Rigging operations
Slips / Trips / Falls
Falling objects
Heat / Cold
Sharps
Repetitive motions
Hand placement
Other Contractors or other work activity in the area
Any other recognized hazard

## Slide 9: Identifying Hazards
Consider:
Physical Actions
Materials
Equipment
Conditions
“What If” questions
Examples:
Worker posture / balance
Potential for being caught in between / pinch points
Hazardous movements
“Struck by” hazards
Suspended loads
Sharp Edges
Employee jewelry

## Slide 10: Evaluate Hazards & Choose Corrective Measures
Evaluation:
Engineering Controls?
Training
Body Positioning
Is a clearance needed?
Sources of the hazard
Slips / Trips / Falls
What PPE should be used?
Corrective Measures:
Must be specific
Should be developed in sequence
Developed at the jobsite
List as many solutions as possible

## Slide 11: Control Methods
Engineering Controls
  Best – Eliminates the hazard
  Always consider first
Administrative Controls
  Example – Work time limits in hot environments
Personal Protective Equipment
  Least effective – Hazard still present
  Last line of defense

## Slide 12: Analyzing High Risk or Specialty Work
Not every task can be adequately covered with one JSA form.
  Specialty work such as, but not limited to, blasting, diving operations, concrete cutting, etc. will utilize the supplemental form and attach to the JSA.
  High risk work such as but not limited to work on hydrogen, ammonia, chlorine, switchyard entry, energized “hot work” will also utilize the supplemental form and attach to the JSA
  Any procedures or special instructions should also be attached and available in the work area for review.

## Slide 13: How to Use the JSA
GF/F receives job assignment
GF/F determines if work is high risk (Risk Calculator) or specialty work – if so, complete the supplement form, obtain any special procedures or instructions and attach as well.
GF/F/Craft conducts task review
The basic task steps are identified and entered onto the JSA
Identify and list the potential hazards
Identify and list the hazard elimination methods used
Review the supplement, if applicable, procedures, instructions, etc.

## Slide 14: How to Use the JSA - Continued
Conduct “Pre-Job” meeting utilizing the JSA
  Should be done in work location if possible
Discuss each task step with crew
Identify competency requirements i.e., certifications, qualifications, license, permits, etc., and list the names on the JSA
ALL sign JSA form (understanding & compliance)

## Slide 15: How to Use the JSA - Continued
Supervision monitors job
Review and modify the JSA if work conditions change, or new hazards are identified.
Review the JSA after lunch, before continuing work
Display JSA in work area until end of shift
Everyone signs off
  Employees shall notify supervision of any injuries that occurred and note in the Post-JSA portion
Complete the Post JSA portion
G/F or designee will review and then submit to contractor Safety for retention – any supplement forms should remain attached and submitted with the JSA.

## Slide 16: JSA– Enhances Safety
The JSA is designed to help front line supervision, and the craft worker be better prepared for a task
More detail in Pre Job Planning
Designed to be easy to implement with minimal training
Basic job steps will now be listed instead of general task description
Will be the standard JSA for all work on a SoCo project.
Helps to ensure all contractors are analyzing tasks and associated hazards in the same manner
Enhances communication between contractors.

## Slide 17
Project Name
Plant site or other designation for location
ERT contact numbers
Job specific info such as foreman, date, time
Task location if needed – such as Unit 1, Elevation 492, or Ash Pond C
Basic task description
Emergency or High Risk Work – attach JSA supplement
Emergency evacuation assembly area info to be filled in based on location of task
The management participation section is to be used by contractor or SoCo management that attends and participates in the JSA meeting
This is your task checklist. Check the appropriate box or write the answer in the space provided. Don’t skip any questions even if they don’t apply.
This is the Pre-Planning section. Use the Risk Calculator to determine risk level. Determine if a clearance is needed for the task and if so, document the clearance number. Answer the 5 what’s.

## Slide 18
List the basic task steps along with associated hazards and control methods. For task steps, be as detailed as possible but don’t just put down the job description. List all know hazards associated with the task – utilize input from the crew – and for safe work methods, be as specific as possible and list as many options as possible. Use additional sheets if needed
Crewmembers will sign in / out here. If additional space is needed, attach additional JSA sheets.
Indicate required PPE, competencies, & procedure/permits required.

## Slide 19
Notes: 19
Let them use it and practice

## Slide 20
Notes: 20
Let them use it and practice

## Slide 22
Notes: 22
Let them use it and practice

## Slide 23
Notes: 23
Let them use it and practice.

## Slide 24
Notes: 24
Let them use it and practice. Have blank JSA’s or just the risk calculator portion to hand out. Describe a common task with enough detail so that the risk can be analyzed and determined.

## Slide 25
Notes: Here is a more detailed description of the Risk Actions.

## Slide 26
JSA Supplement for High Risk or Specialty Work
Notes: For specialty or high risk work, use the JSA supplement to identify additional concerns and control methods. Attach the JSA supplement to the JSA and turn it in with the JSA upon completion of the work.

## Slide 27: Prepare a JSA for a Simulated Task
(List a task that is typically performed by your company. Include any environmental factors or other interferences that may be typically encountered. – Review the JSA’s produced and coach as needed)